## Slide 1: Technology Comparison Update
Sven Vahsen (Hawaii)

## Slide 2: Overview of Simulation Steps
Cosmology Simulation [or delta functions]
Simulation of nuclear recoils and resulting ionization
Charge transport (drift, diffusion, reabsorption etc. )
Other detector technologies
WIMP + neutrino recoil distributions
Ciaran O’Hare
Cosmin Deaconu
Sven Vahsen
Sven Vahsen
Kentaro Miuchi
w/ help from technology experts
(Tom Thorpe will also get involved)
Readout plane simulation
Wires
Strips
Optical
Pixels
Mu-pic
Discovery variables
Ionization clouds
Discovery cost
Low pressure Gas TPCs

## Slide 3
Cosmology Simulation [or delta functions]
Simulation of nuclear recoils and resulting ionization
Charge transport (drift, diffusion, reabsorption etc. )
Other detector technologies
WIMP + neutrino recoil distributions
Ciaran O’Hare
Cosmin Deaconu
Sven Vahsen
Readout plane simulation
Wires
Strips
Optical
Pixels
Mu-pic
Discovery variables
Ionization clouds
Discovery cost
Pixels
Mu-pic

## Slide 4: Cosmology Simulation
WIMP Input parameters:
  Target Nucleus
  WIMP mass
  WIMP halo model parameters
  Interaction details (SD, SI, other)
  Form factor / nuclear physics
Neutrino Input parameters: ?
Ciaran will provide recoil vectors in format px, py, pz, event time. We agreed to start with a WIMP recoil test event sample based on:
  Flourine
  M_WIMP = 1, 10, 100, 1000 GeV/c^2
  SHM with v_0 = 220 km/s and v_esc = 533 km/s and rho_0 = 0.3 GeV/cm^3.
  From Ciaran:
    “For the form factor/nuclear physics. In the past we've usually adopted a simple Born form factor for F spin-dependent. It should be fine to use this for now, at the very least it will agree with previous work. In my last paper with Bradley Kavanagh we were a bit more rigorous and took some more up to date form factors and values for the spin contents so if we wanted something a bit more accurate (but a bit more involved) then I already have that in place.
    For the recoil time what I usually do is just use a year's running time and then to get results for different exposures I just need to vary the detector mass factor. The events are a lot easier to handle like this, and it turns out it has the same effect as if you were changing the length of time by the same factor. Then I can just label the recoil time in days since Jan 1st (or whenever).
    Event generation takes no time at all, I can generate as many events as you need really. I would imagine quite a lot of events (closer to a million) would be needed to smoothly represent the distribution though since it is quite spread out in the lab frame thanks to the rotation of the Earth. “
In addition to WIMP/neutrino recoils, will also use recoil distributions that are delta functions in theta, phi, E (in steps of E)
  compare energy threshold for directionality of different technologies: how many recoils required to detect isotropy at five sigma?
  Interesting in itself, and validates downstream simulation steps

## Slide 5: Recoil Simulation
Input parameters
  Gas composition
  Gas pressure
   affect straggling, stopping power (recoil length)
Use SRIM. Many possible approaches, showing four. Top is most precise. Bottom is fastest.
  Create large number of individual 3D recoils for each recoil energy bin in SRIM, draw recoils from appropriate sample.
  Create large number of individual 1D recoils for each recoil energy bin in SRIM, draw recoils from appropriate sample.
  Create 1D SRIM dE/dX p.d.f. for largest possible recoil energy. Use this single pdf to create recoils of all energies.
  Create 1D SRIM dE/dX p.d.f. for largest possible recoil energy, numerically convolute it to obtain 3D p.d.f. for recoil charge distribution that includes detector simulation as well. Use this single pdf to create recoils of all energies.
  Sven has implemented 3 and 4 for D3 (TPC w/ pixel readout) (they are largely equivalent)
  Cosmin has implemented 1 for DMTPC (TPC w/ optical readout)
  Plan
    compare 1 with 3 to validate both and assess impact of straggling on our results.
    use 1 if fast enough. Otherwise 4.

## Slide 6: TPC Charge Transport & Readout Plane Simulation
“Gas” Input parameters:
  E –field strength
  Drift length
  Gas mixture
  Gas pressure
  Gas purity
  affect drift velocity, diffusion (L/T), charge losses during drift
Readout plane input parameters
  Gain, noise, x,y, segmentation, shaping time, digitization specs, etc (list depends on technology)
For electron drift gases, Magboltz can accurately calculate drift velocity, diffusion
Not fully sure what to do for NID gases
    Can probably get most quantities from measurements by Dinesh
      velocity, diffusion (reattachment effect included?), max gain, gain resolution
    Not sure if we can reliably extrapolate to lower pressures.

## Slide 7: D3 Toy Monte Carlo (“method 3”)
Simulates every single electron in python (precise but slow)
Features with “Y” will be included
Features in green have been implemented
Physical Effect | Included in toy MC?
dE/dX | Y
W | Y
Fano factor | Y
electron clusters | N ?
Recombination | N ?
Longitudinal, transverse diffusion in drift gap | Y
drift velocity in drift gap | Y
reabsorption in drift gap (impurities, space charge etc) | Y
GEM gain | Y
Gain resolution/uniformity | Y / N
gem hole spacing | Y
gem shower shape | rough approx.
diffusion (l,t) in transfer gap | Y
diffusion (l,t) in collection gap | Y
time spent in transfer, collection gaps? | rough approx.
quantization into pixel x,y positions | Y
quantization into pads | Y ?
detailed modeling of pixel arrival time distribution? | Y ?
quantization of charge arrival time into BCIDs | Y
charge, treshold, TOT scale -> TOT in each pixel | Y (COT)
hitor modeling | Y
X (mm)
head
tail
dE/dX
Po-210 α-particle
in He:C02 (70:30)
Bragg peak

## Slide 8: Example of TPC simulation: one event
Double GEM pixel TPC
750 keV He-recoil in HeC02
Drift: 5 cm
gain = 900 per GEM

## Slide 9: generated
Simulating individual electrons, but quantizing when visualizing
Quantization: (500μm)3

## Slide 10: post drift

## Slide 11: post GEM1

## Slide 12: post transfer gap

## Slide 13: post GEM2

## Slide 14: post collection gap

## Slide 15: above threshold
now with finer quantization - equal to that of pixel chip
npoints = 17443

## Slide 16: above threshold
rendering of box edges turned on

## Slide 17: fully digitized
npoints= 1211

## Slide 18: fully digitized (non transparent)

## Slide 19: 2nd Simulation approach
Recoil p.d.f. that incorporates detector effects (from charge transport and readout plane)

## Slide 20: Charge Cloud PDF – before detection
dE/DX distribution from SRIM – quantized
Each point charge then numerically convoluted with a Gaussian to account for charge diffusion during drift & detector resolution

## Slide 21: Charge Cloud PDF – after detection
Charge integrated in the drift direction pseudo-analytically, and detector threshold applied
59 s per space point [in python]

## Slide 22: Summary
Technology comparison involves integration of multiple simulation codes
Simulation of Cosmology, Nuclear Recoils, Charge propagation, TPC+Mu-Pic readouts exists
Next steps, roughly:
  Complete exercise all the way to end (cost / discovery) w/ pixel TPC
    delta function recoil distribution for debugging
    SF4 at 34 torr (same density at SF6 @ 20 torr + we have exp. data for validation)
  Add Mu-pic w/ Kentaro, then other readout plane technologies
  Simulate SF6 at ~ 20 torr
  Switch to WIMP / neutrino cosmology as input
  Tidy up code and put in Git
Still pondering:
  Best discovery variables for TPC that don’t fit tracks
  How to deal with non-TPC technologies

## Slide 23: Exerimental data

## Slide 24: Simulation Approach
Simulating every single electron at all stages of detector
  millions per track. Slow, but doable.
Visualizing + storing only quantized charge distribution
  same format as final data
  at different stages of simulation
  same binning as pixel chip or different
    crucial for visualizing and fitting before digitization

## Slide 25: 60 keV: can you see the head/tail ?
(same event, after 2k electron pixel threshold)

## Slide 26: 60 keV: can you see the head/tail ?
(same event, after 2k electron pixel threshold)