## Slide 1: Time-to-Amplitude Converter
Presented by: Jon Itokazu December 10th, 2021
PHYS 475

## Slide 2: Overview and Specifications
26 ps resolution Time-to-Digital Converter for Time-of-Flight applications.

## Slide 3: Schematic and Overview
For testing purposes only
Note: Due to issues, a SN74AHC4066 was used in place of SN74AUC1G66 for prototyping

## Slide 4: Simulation vs. Measurement
Measurement was taken at Vcap
  discrepancy at ramp peak due to oscilloscope probe causing the sampling capacitor to discharge
Measurement and Simulation information
  Time Div. → 25 ns/div
  Volt. Div. → 100 mV/div
  Vmax(sim:ideal) → 496 mV
  Vmax(sim:non-ideal) → 525 mV
  Vmax(sim:measured) → 512 mV
Vcap

## Slide 5: Capacitor Ramp Linearity
Linear Region
Non-Linear Region
Non-Linear Region

## Slide 6: Future Works
Improve linear range
  switches with better isolation to reduce leakage current
Reduce Noise
  Survey for alternate parts with better noise performance
  Implement on board using layout techniques
Create circuit at the transistor level

## Slide 7: Q&A
Thank you for your time and attention
? The floor is now open for questions