## Slide 1: Cooperative monitoring of reactors using antineutrinos Niche but important applications in nuclear arms control and nonproliferation – which, who knows, might one day lead to World Peace
Adam Bernstein, Vienna Center for Nonproliferation and Disarmament
Festschrift für Professor John G. Learned 2025

## Slide 2: Foreshadowing
“I don’t say that the neutrino is going to be a practical thing, but it has been a time-honored pattern that science leads, and then technology comes along, and then, put together, these things make an enormous difference in how we live.”
Fredrick Reines, winner of the Nobel Prize and co-discoverer of the neutrino NYT interview, 1997
http://library.lanl.gov/cgi-bin/getfile?00326606.pdf

## Slide 3: The obstacle to making neutrinos a practical thing for nuclear security
John H. Gibbons, Clinton head of Office and Science and Technology Policy, discussing how to deal with U.S. and Russian plutonium declared surplus to military needs, 1994
“This is one of the most challenging policy problems I've come across, weaving together issues of technology, security, environment, energy, and international politics.
Policy problems can’t be solved by physicists, engineers or technology alone

## Slide 4
Cooperative monitoring concepts sorted by distance
10 km
100 km
100 m
detector distance from reactor
depth: 100-1000 m
detector mass: 1 kiloton – 500 kilotons
dwell times: months to 1 year
applicable in low-to-medium background regions only
depth: 10-100 m
detector mass: 5- 3000 tons
dwell times: weeks to months
applicable worldwide
Near-field
Mid-field
Far-field
power/burnup monitoring
exclusion for >50 MWt reactors
exclusion only for >50 MWt reactors
onsite reactor monitoring
depth: surface/a few meters
detector mass 1-10 tons
dwell times: hours to months
applicable worldwide

## Slide 5
Possible uses for antineutrino-based monitoring
NPT and Confidence
Cooperatively verify a reactor shutdown or absence of reactors from outside a site (NPT AP)
Check status of surplus plutonium burning in civil reactors (Pu disposition)
Advanced Reactor Fuel Safeguards
Monitor reactors with e.g. bulk fuel or opaque coolants
Monitor multiple small modular reactors on a site
Naval Reactor Verification
Verify reactor core presence/enrichment in a non-nuclear weapon state submarine
Cogswell & Huber, PRL 128 241803 (2022)
Carr, et al, Science & Global Security (2019)
Non-intrusive, persistent, unattended, quantitative estimates of key reactor properties
near to mid-field applications
mid and far-field application
See https://neutrinos.llnl.gov/sites/neutrinos/files/AAP2018-IAEA-Anzelon.pdf for existing IAEA reactor safeguards methods
https://arxiv.org/abs/2308.01306

## Slide 6: Near-field cooperative monitoring

## Slide 7: R&D Timeline for Near-field Monitoring
1990
Birth of the idea:
Neutrino ’77, Baksan (maybe ’75 ?)
2004:Early (the first ?) US workshop on Neutrinos and Arms control, J. Learned, UH
2006 onward Applied Antineutrino Physics workshops France, Japan, US, Brazil, India, UK,
Country
USA
Japan
UK
Italy
France
Japan
CA/US
Brazil
Japan
USA
India
Russia
‘Cambrian explosion’ for
monitoring
detectors
Theoretical case studies (Huber, others)
coherent-scatter based reactor monitoring (Hagmann TNS 51, 5, 2004)
All basic ideas explored with IBD detectors
The Rovno era
surface-level detection
PROSPECT CHANDLER
Conus+
coherent scatter
measurement
1980
2000
2010
2020
IAEA workshops on antineutrino-based monitoring
🏈
🏈
🏈
basic ideas re-explored - some simplifications and attention of the IAEA
Gd-scintillator donated by F. Boehm/Gratta from Palo Verde experiment
IAEA safeguards applications
Bernstein JAP. 91, 4672–4676 (2002)
SONGS

## Slide 8: Current IAEA safeguards practice at reactors (220 worldwide)
(1–1.5 years)
(months)
(forever)
Check declarations
Item accountancy
Containment and surveillance
Gross defect detection
Item accountancy
Containment and surveillance
(months to years)
Operators only declare fuel burn up and power history
No direct Pu inventory measurement is made unless the fuel is reprocessed
Can antineutrino detectors provide real-time inventory estimates?
Reactor
Onsite Fuel Storage
Reprocessing
U Pu Radwaste
Waste Repository
Check declarations
Bulk accountancy
Japan only

## Slide 9: An early description of near-field reactor monitoring - Neutrino ‘77 conference, Baksan
Borovoi, A.A., Mikaélyan, L.A. Possibilities of the practical use of neutrinos. At Energy 44, 589–592 (1978). https://doi.org/10.1007/BF01117861

## Slide 10: Large reactor flux overcomes the small cross-section giving tractable rates
Detected rates are reasonable
1017 antineutrinos per square meter per second at 25-m standoff
6,000 events per ton per day with a perfect detector
Modern detectors (e.g. NEOS) 2000 or more per ton per day
Reactors emit huge numbers of antineutrinos
6 antineutrinos per fission from beta decay of neutron-rich daughters
1021 fissions per second in a 3 GWt reactor
About 1022 antineutrinos are emitted per second from a typical PWR unattenuated and in all directions

## Slide 11: Reactor antineutrino energy spectra, convolved with changing fission fractions, produce the “burnup effect”
Energy spectra vary with isotope
For each isotope, fission rates vary with time
Events/MeV/fission (relative frequency)
First order: ~10% Varying contributions from Pu/U isotopes
Zeroth order:
reactor power
235U
239Pu

## Slide 12: Results from a nonproliferation demonstration in San Onofre California
Measure thermal power to 3% in one week
Detect switch of 70 kg Pu with equivalent amount of 235U in three months
Determine reactor on/off status within 5 hours with 99.9% C.L.
J. Appl. Phys. 103, 074905 (2008)
J. Appl. Phys. 105, 064902 (2009)
J Appl. Phys., 109 11, Jun 2011
0.6 ton liquid scintillator detector
Total footprint ~ 3x3x3 meter
25 electronics channels
NIM A 572, 2, (2007)

## Slide 13: Antineutrino rate and shape measurements reveal properties of the core
5 ton detector
3 GWt core
25 m standoff
Sensitive to an 8% change in MOX composition in 150 days
arxiv:1612.00540
arxiv:1403.7065
5 ton detector
40 MWt core
17.5 m standoff
Sensitive to a change of 7 kg of Pu at > 5 sigma
Comparison of two spectra with midpoints on cycle day 45 and day 315
Comparison of relative nubar rates versus time for different core types
(Plutonium disposition)
(North Korean Reactor monitoring)

## Slide 14: What about coherent scatter to shrink detector size or increase rates ?
C. Hagmann and A. Bernstein, Two-phase emission detector for measuring
coherent neutrino nucleus scattering, IEEE TNS 51, 2151 (2004)

## Slide 15: Near-field monitoring summary
In the near-field (<100 m or so) it has been proven since Rovno/1980’s that antineutrino detectors can be used to determine fissile inventories and power levels at reactors
Reliable long-lasting detectors are deployable now
Further steps, such as mobile detectors and better S/B above-ground are useful technical R&D
Policy analyses are essential to gain the interest of the user community
Political will and the attention of the policy community are the main missing ingredients

## Slide 16: Mid and Far Field cooperative monitoring

## Slide 17
  Site-wide exclusion of > 50 MWt reactors
    Independent information about presence or absence of small reactors
    Confidence-building measures to support and complement NPT and future treaties
    Threat of discovery helps deter undeclared reactor construction and operation
  Monitoring of advanced reactors
    Fill known safeguards gaps
      Small modular, Pebble bed, and Molten salt reactors
    Provide non-intrusive and independent site-wide power and burnup information out to several kilometer standoff
Mid-to-far-field - cooperative discovery, exclusion and monitoring of reactors
Examples of possible mid-to-far-field deployments
Greater standoff or lower reactor power  Reduced flux  larger detectors and less detailed information

## Slide 18
Mid-to-far-field antineutrino-based monitoring systems offer unique capabilities
  Less intrusive than near-field deployments or onsite inspections
  Potential for wide-area coverage
    Sensitivity ranges from 100 m to a maximum of 100 km
  Persistent
  Definitive confirmation of absence of reactor activity
  Antineutrino emissions can’t be shielded
  Opportunities for scientific collaboration with inspected party
    e.g., Confidence-building measures
“take every precaution to protect commercial and industrial secrets and other confidential information coming to its knowledge and implementation of the Agreement”
“avoid hampering economic and technological development”
”avoid undue interference”
NPT Additional Protocols emphasize minimizing intrusiveness and burden to the state
No other reactor monitoring/exclusion technology – radionuclide detection, satellite imagery, onsite inspections - enjoys this unique set of features

## Slide 19: Timeline for Mid/Far-field Monitoring concepts
2000 2005 2010 2015 2020
‘01: Bernstein et. al.
Gd-doped water for CTBT monitoring applications
Conclusion: not worth it for the 1 G$ price of entry
KamLAND
‘03 - reactor measurement at 200 km
’03: Dreaming big: John Learned considers the benefits of a gigaton array of monitoring detectors
‘10: Lasserre et. al – PRC ‘Secret Neutrino Interaction Finder’ marvelously detailed treatment of reactor and non-reactor backgrounds
‘09-10 - LLNL/SK/EGADS Physics and engineering Gd-H2O demonstrators (1-200 tons)
relevant experiments
relevant
analyses
‘17: Carr et. al – PR Appl. 10 ‘Seismically cued antineutrino detectors’
Modest improvement on ‘01 results
AGM 2015 Usman/Learned
geoneutrino.org/reactors S. Dye
Palo Verde ‘98 - reactor measurement at
~1 km
WATCHMAN: 1 kT Gd-doped water devoted to reactor monitoring
Super-K_Gd: 50 kT Gd-doped water
X
JUNO: 20 kT scintillator

## Slide 20
The world’s reactors form a limiting and essentially irreducible background for far-field exclusion and discovery applications
Due to the variability in backgrounds, the minimum dwell time and detector size changes substantially across the globe Sensitivity is highest in the low and medium background regions of the world
results from https://reactors.geoneutrinos.org/, S. Dye, A. Barna
https://arxiv.org/pdf/1510.05633.pdf
This is an enormously useful and convenient tool !

## Slide 21
Liquid media in homogenous or modestly segmented volumes are most relevant for mid-to-large scale antineutrino detectors
Medium | Advantages | Disadvantages
Liquid scintillator | Proven design Fewer light sensors compared to alternatives Best for monitoring applications requiring good energy resolution | Combustible Must be transported or manufactured onsite
Gadolinium- doped water | Nontoxic Readily available Large detectors possible due to high light transmissivity Attractive for discovery/exclusion applications | Inferior background rejection Poor energy resolution More light sensors than alternatives
Gadolinium, water, and scintillator mixtures (water-based liquid scintillator) | Reduced environmental impact compared to pure scintillator Possibly improved background rejection compared to water Mixture adjustment provides performance flexibility | Least mature technology
The KamLAND
Liquid Scintillator Detector
(1000 ton mass)
The Super-Kamiokande Gadolinium-doped water Cherenkov Detector (~50,000 ton mass)
The Palo Verde Gadolinium-doped Scintillator detector
(180 ton mass)

## Slide 22
The ideal and the real – current and future limitations on far-field detection of 50 MWt reactors in < 1 year
Liquid scintillator
Only reactor and geoneutrino backgrounds
A 3.3 MeV energy cut is applied to remove geoneutrinos – detector records all reactor antineutrinos above this energy
(Gd-H2O detector, 40% PMT coverage)
Detailed background model: ambient radioactivity; muogenic neutrons/pions/gammas , other reactors, geoantineutrinos
Full Monte Carlo including photon tracking and individual event reconstruction
Low
background
regions
High
background
regions
10 km
1 kt
1 month
1 kt
4 month
20 km
1 kt
5 month
5 kt
1 year
50 km
10 kt
1 year
1000 kt
1 year
10 km
Not analyzed
1.4 kt
1 year
100 km
100 kt
1 year
Not possible with this design in 1 year
20 km
1.4 kt
1 year
25 kt
1 year
100 km
Not possible with this design in 1 year
Not possible with this design in 1 year
35 km
60 kt
1 year
Not possible with this design in 1 year
Detector fiducial mass and dwell time results
Ideal detector, simple model
Plausible detector, detailed model
Ideal detector
State-of-the-art detector
See Slava Li paper - https://arxiv.org/abs/1907.08891

## Slide 23: The gadolinium solution permits the use of the (possibly) more scalable water-based detector
    ve + p = e+ + n
    Gadolinium nucleus captures neutrons with high efficiency and creates an intense flash of Cherenkov light
    The signal is two flashes of Cherenkov light, close in time (~100 μsec) and location (~5 cm)―the “antineutrino heartbeat”
    Method reduces backgrounds by several orders of magnitude
    Gadolinium-doped Water Cherenkov technology offers path to 100–1000 kiloton antineutrino detectors
    First proposed by Bernstein in 2001 Science & Global Security 9, 235 (2001)
    Experimental verification in 2009 LLNL: NIMA 607 (3), 21 (August 2009) Super-K: Astroparticle Physics 31(4), 320–328 (May 2009)
10.1016/j.nima.2014.10.028
Neutron signal in LLNL Gd–H2O detector
Notes: 2.2 MeV gamma just form proton neutrino scattering
Measurement of the positron energy determines the neutrino energy since
E𝜈 = EE + 1.3 MeV
Gd cross section for thermal neutrons 49,000 barns compared to .33 barns for Hydrogen. At .2%, 90% of captures are on Gd (.2% on Chlorine, rest on Hydrogen). Capture occurs in about 3 microseconds and about 4cm.
In SK, at energies below 3 MeV, background singles rates (i.e. a capture of a single neutron or emission of a gamma) are much too high to detect neutron captures in isolation, however by using this reaction and by requiring a very tight time and position coincidence between the positron and follow-on neutron, nearly all captures on Gd can be detected.
Reactor neutrinos at SK: total rate from inverse beta decay scaled from KAMLAND is about 30/day. With a coincidence signal, it would be possible to identify real events as low as EE = 2.5 MeV covering most of the reactor spectrum. Precision measurements of the
neutrinos from all of
Japan’s power reactors
(~5,000 events per year)
Solar antineutrino flux is < than 1% of predicted electron neutrino flux. Requiring a neutron coincidence would greatly reduce backgrounds giving a sensitivity of about .01%
23

## Slide 24: The WATCHMAN demonstration
Detect the ON/OFF power cycle of a single reactor:
at 10-25 km standoff
with a kiloton-scale Gd-H2O detector
at 3 sigma confidence level
Choose water based on cost and scalability
Doping the water with gadolinium greatly increases sensitivity to inverse beta interactions of antineutrinos
WATCHMAN: A WAter CHerenkov Monitor of Antineutrinos
Main Project Objective:

## Slide 25: The WATCHMAN collaboration, ~2014 (ish)
32 collaborators
9 Universities
4 National Laboratories
Co-spokespersons:
Adam Bernstein, LLNL
Mark Vagins, UC Irvine/Tokyo University
The
WATCHMAN Collaboration
AWE
J.Burns
LLNL
A. Bernstein
M. Bergevin
S. Dazeley
UC Berkeley
G. Orebi Gann
UC Davis
R. Svoboda
UC Irvine
M. Vagins
U. Michigan
I. Jovanovic
U. of Sheffield
M. Malek
N. Spooner
L. Thompson
U. Pennsylvania
C. Mauger
BNL
M. Yeh
Iowa State U.
M. Wetstein
Penn State U.
D. Cowen
STFC–Boulby
S. Paling
U. Hawaii
S. Dye
J. Learned
Water attenuation measurements
Neutron spectrometry at multiple depths
(MARS spectrometer)
Tagged muogenic neutron multiplicity measurements
(WATCHBOY)
Gd-water materials testing
WbLS development
LAPPD studies
PMT purchase and testing

## Slide 26: After several reversals, WATCHMAN transmuted into a long-term R&D program
Hartlepool reactor announced its shutdown for 2024 (prematurely)
Cost estimates in the UK where raised substantially against original $40 M pricetag
Fairport/IMB site purchased by venture capital group with no interest in nonproliferation demonstration
Sponsor decided that an R&D program was preferable to a demonstration
An enduring neutrino-related set of activities continues – advanced PMTs, better way to measure attenuation, WbLS etc. – see Slava’s talk

## Slide 27: My prescription for an achievable next step
A demonstration involving a Non-Nuclear and Nuclear Weapons state
  Historical precedent – UK-Norway initiative on warhead disarmament monitoring
Propose near and mid-field antineutrino deployments as a demonstration
De-emphasize R&D until the deployment is complete
Finally, propose to Iran, North Korea or other adversary as a scientific diplomacy initiative – this I consider to be the ultimate success for this technology

## Slide 28: Monitoring Nuclear Tests
2001 and 2019 studies – not competitive in sensitivity or cost against existing CTBT methods
Very limited utility for ton-scale test exclusion
No utility for differentiating sub-critical from critical tests
May have utility for diagnostics of kiloton-scale tests (a proliferant activity in violation of the CTBT)

## Slide 29: Coincidences in Nature
…the (Up-Down Cosmic Ray) asymmetry is indeed maximal, which makes it appear that we are very lucky that the earth size and cosmic ray energies are “just so” to produce this dramatic effect. This appears to this author to fall in the category of lucky co- incidences, such as the angular diameter of the moon and sun being the same from earth. .. The phase space for “coincidences” is very large, and we humans are great recognizers of such patterns.
‘Introduction to Neutrino Astronomy’, John Learned, 1999

## Slide 30: Coincidences in Nature
Friedrich Hundertwasser Austrian painter
architect
freethinker
Hundertwasser rendering of the sun in oil
Learned-inspired rendering of the sun in neutrinos
John Learned American Physicist
woodworker freethinker

## Slide 31: Backup slides

## Slide 32: An Historical Artifact: J. Learned vision for remote monitoring applications, circa 2007

## Slide 33: Practicality can mean many things
Astrophysical
Accelerators
Nuclear Reactors
Earth’s Atmosphere
Sun
Supernovae
Earth’s Crust and
Mantle
Big Bang
Nuclear Explosions
Slide adapted from JGL
Notes: These other studies also count as applications – neutrinos are effective probes of the universe
To pursue neutrino solar studies or geophysics, you have to learn about the general properties of the sun or Earth
To pursue nonproliferation and disarmament, you need to learn about nuclear security

## Slide 34: The Problem for CNS: ‘Good-ol’ inverse beta’* actually works pretty well
Detector feature | IBD Demonstrated | IBD plausible | Argon | Germanium | Phonon-counter
Footprint with shield | 3 m | 1.5 m | 2 m | 1.5 m (CONUS+) | 0.5-1 m ?
Mass for 100 cpd at 25 m from 3.4 GWt | 16 kg | 16 kg | 15 kg | 5 kg | 50 gram
Energy threshold | 1.8 MeV (nubar) |  | > 2 e-, ~200 eV threshold | 50 eV (CONUS+ threshold is 160 eV) | ~meV scale
*Petr Vogel, CalTech
Achievable thresholds for CNS detectors prevent realization of the advantage of the higher cross-sections

## Slide 35: Spectroscopy with (ionization-based) CNNS is underwhelming
No-threshold property doesn’t help much
Few ionizations – ~10x worse energy resolution than IBD detector
CNNS Spectrum must be unfolded, IBD spectrum is directly proportional to nubar energy

## Slide 36: A somewhat less practical thing: ‘mid-to-far-field’ reactor monitoring
Discover, or exclude the existence of, operating reactors
Mid/‘Far’: more than 1 km, out to perhaps 100 km – varying degrees of access
‘low’ statistics: a few events per week month, year
Reactor power ~50 MWt – roughly generating 8 kg/one Significant Quantity per year
Technology: Variations on KamLAND, Super-Kamiokande, Borexino and other large detectors

## Slide 37: Site and configuration choices
 | Option 1 | Option 2
Reactor Location | Perry, Ohio, United States | Hartlepool, England, United Kingdom
Thermal Power (MWt) | 1 x 3875 | 2 x 1500
Detector Location | Morton Salt/IMB mine Painesville, Ohio | Boulby underground science lab, Boulby, England
Standoff | ~13 km | ~25 km
Overburden (mwe) | ~1500 | ~3000
Signal Events | 110 per month | 11 per month
Background Events | 50 per month | 20 per month

## Slide 38: 1980s - the remarkable deployment at Rovno
core center
18 m
detector center
The ideal monitoring experiment !
Reactor and Earth shield cosmics
Detector is close to the core but in a relatively low radiation environment
1400 MWt reactor (VVER 440)
18 m from core
18 m of overburden
500 l liquid scintillator (Gd-doped)
84 PMTs

## Slide 39
Other challenges and mitigations
Challenge | Mitigation
Excavation costs | Improve background rejection to reduce depth
Detector costs | Reduce the number and/or increase performance of the dominant cost item – light sensors Increase the usable fraction of the detector volume
Time to deploy | Use pre-built modules and existing excavation
Public, political and nonproliferation community acceptance | Host country: explain to its citizens the scientific and diplomatic benefit of the deployment All: use internationally accepted techniques to validate data All: Perform a field demonstration to provide a real-world example to the policy and technical communities (e.g. UK/Norway Initiative, Black Sea Experiment, others)
https://scienceandglobalsecurity.org/archive/sgs17belyaev.pdf
https://www.gov.uk/government/publications/uk-norway-initiative-on-nuclear-warhead-dismantlement-verification--2

## Slide 40: Long-range reactor antineutrino detection is feasible now with liquid scintillator
Per month:
16 reactor antineutrinos
1 background event
From 130 GWt of reactors
~3% of signal from South Korean reactors @ 400 km standoff
1000 tonnes scintillator 1000 m depth
The KamLAND detector
South Korea

## Slide 41: Today’s Water Cherenkov detectors are 50x larger than scintillator detectors, but can’t distinguish neutrino from antineutrino
The Super-Kamiokande water Cherenkov detector
    ve + p = e+ + n
    ve + e-= ve + e-
Identical signals from both processes: a single flash of
Cerenkov light
Inverse beta decay from reactor
Elastic scatter
(solar neutrinos, reactors)
    ve

## Slide 42: Possible users
The International Atomic Energy Agency – responsible for monitoring nuclear facilities in all Non-Nuclear Weapons States (as defined by the NonproliferationTreaty)
  Not relevant for current crop of reactors
  Potentially useful for some new reactor types/special cases
  Fixed IAEA standards for time to discover, material mass, confidence level (95%)
Pairs/groups of States interested in “Confidence-Building Measures”
  “Confidence-building Measures” are non-treaty-based, joint activities meant to lessen tensions between states
  The Iran deal, monitoring North Korea’s nuclear program, others
  Scientific diplomacy and technical engagement are key features
  No fixed performance standard
Signators to the Comprehensive Test-ban Treaty (most countries)

## Slide 43
A comparison of reactor exclusion and discovery techniques
 | Non-cooperative methods |  | Cooperative methods | Cooperative methods
 | Satellite imaging | Radionuclide detection | Onsite inspections | Antineutrino detection
Advantages | effective at seeing plumes/heat signature/evidence of industrial activity repeat visits possible assets already fielded | Can qualitatively confirm the existence of reactor Cross-border detection possible | Direct observations of activity/non-activity Quantitative estimates possible (with suitable equipment) | Exclusion, thermal power and/or fissile material measurement or constraint possible with known confidence Unaffected by weather or geography does not depend on accidental release of radiation absence of evidence is evidence of absence
Limitations | absence of evidence not conclusive Cueing often required Continuous or accurate power measurement not practical May be obscured by weather Burial/heat removal can hide reactor operations | absence of evidence not conclusive Localization is difficult Depends on accidental release of activity from reactor Quantitative estimate of reactor power is difficult Detection complicated or frustrated by weather conditions | absence of evidence not conclusive Search is limited to agreed access areas during limited time periods (c.f. Iraqi inspections*) | Maximum geographical coverage of ~10,000 sq kilometers possible only with ~500 kton detectors Overburden requirements increase with distance Expense increases with distance Siting options highly case-dependent
*https://www.armscontrol.org/act/2002-10/features/iraq-chronology-un-inspections