## Slide 1: Neutrinos in Action: from miniTimeCube to Shaping the World Nonproliferation Landscape
Workshop on Ghost Particle Hunting:
Neutrino Physics and its Applications to World Peace
University of Hawai`i
April 28 – May 3, 2025
Viacheslav A. Li
Rare Event Detection group
Lawrence Livermore National Laboratory
neutrinos.llnl.gov
La__

## Slide 2: My first interaction with John
From: John G. Learned
Date: Fri, Dec 17, 2010
...
I have a small project building a very nice
2 liter neutrino detector for use near reactors....
it hopefully opens the door to a new type of anti-electron neutrino detection (including directionality).

## Slide 3: My first interaction with John
From: John G. Learned
Date: Fri, Dec 17, 2010
...
I have a small project building a very nice
2 liter neutrino detector for use near reactors....
it hopefully opens the door to a new type of anti-electron neutrino detection (including directionality).

## Slide 4: Time
2011
2018
2025
University of Hawai`i — grad school
Lawrence Livermore National Laboratory
LLNL aboveground detector R & D:
segmentation + 6Li + PSD + plastics
SANDD
ROADSTR
MAD
Water-based detection
AIT/WATCHMAN (see A. Bernstein’s talk)
BUTTON (see J. Coleman’s talk)
LAPPD/electronics
Directionality (MTV consortium)
miniTimeCube
Neutron Time Camera
NuLat (see B. Crow’s talk)
CASC-NN*
Call me John.

## Slide 5: Nuclear reactors emit enormous amounts of νe
miniTimeCube = 1536 pixels looking into 2-liter scintillator
Inverse β decay since the 50s
Idea to use fast photosensors and fast electronics to detect first-photon arrivals: particle ID / imaging

## Slide 6
Idea and simulations

## Slide 7: Construction and calibration
Use Gary Varner’s Belle electronics
Couple it with Photonis MA MCP-PMTs
Reality is not that simple
me
Using air duct to raise mTC.
Do not do it in your lab.

## Slide 8: miniTimeCube — ahead of its time Real data and deployment at NIST research reactor
Muon going through mTC
Distance 5 m to the core
Compact 20 MW core
Group meeting circa 2014
Rev.Sci.Instrum. 87 (2016) 2, 021301
AIP Adv. 8 (2018) 9, 095003
AIP Adv. 9 (2019) 3, 035301
While the project did not succeed in detecting neutrinos
in its first outing, many important lessons were learned.

## Slide 9: Cube made by John
This was the most used tool in the mTC era.
https://www.phys.hawaii.edu/~mtc

## Slide 10: Joining LLNL
Visit LLNL.gov to learn more
LLNL is now home to the world’s largest supercomputer El Capitan
The only place on Earth that can achieve ignition repeatedly
Nuclear nonproliferation and strategic deterrence — key missions

## Slide 11: 6Li and PSD in plastic scintillator and its advantages
This part of the talk will focus on the path towards realization of a reactor antineutrino detector.
Invented at LLNL in 2010s by N. Zaitseva
Material scale-up by Eljen to multi-kg pieces
Basis for multiple neutron and neutrino systems at LLNL
Main advantages:
6Li — localized capture location
PSD — background rejection based on particle ID
Plastic — ease of handling and deploying

## Slide 12: Essence of Pulse-shape sensitivity and lithium-6
1H
3H
6Li
n
4He
e+
e–
Prompt Light
[Electronic Recoil for PSD]
Delayed Light
[Nuclear Recoil for PSD]
γ
γ
6Li concentration
0.1% by weight:
~88% captures on 6Li
~12% captures on 1H
2.73 MeV
2.05 MeV
Quenched energy ~0.5 MeV electron equivalent
511 keV
511 keV
νe
Thermal-Neutron Captures
Nuclear recoils
Electronic recoils
Data obtained with a 252Cf fission source
Tail and Total time windows
define PSD factor
PMT
Scintillator
PMT

## Slide 13: Scintillator Formulation Decade of R&D
Monomer – styrene or vinyl toluene
  [Building block for a scintillating polymer]
PPO – primary dye, also provides PSD
Secondary dye – shifts light to deep blue (425nm)
6Li salt – provides 6Li
Co-monomer – methacrylic acid organic compound to dissolve 6Li salt
Cross-linker – helps polymerization achieve hard structure
Antioxidant – prevents degradation from air exposure
Exacting temperature control during curing in glass molds
Co-monomer
for solubility
Primary dye
Secondary dye
Monomer
for matrix
6Li salt
Co-monomer for crosslinking
Add components
Control:
predissolution
weight percentage
temperature
Add initiator for curing
Control:
• temperature ramp
• curing time
• oxygen content
First stable 6Li-doped PSD scintillators developed at LLNL.
Zaitseva et al. NIM A729.
R&D: stability, formulation, doping level, PPO level, etc.
Mabe et al. NIM A806.
SANDD: LLNL Exploratory Research to study feasibility of 10-liter detector and PSD with SiPM-array readout
Sutanto et al. NIM A1006.
Ford et al. NIM A1050.
Arrival of new material for MAD 2D
Material scaling at Eljen: EJ-299-50.
Roca et al. arxiv:2405.19573.
Plastic scintillators with efficient neutron/gamma pulse shape discrimination.
Zaitseva et al. NIM A668.
SANDD: SiPM-array readout and PSD
Li et al. NIM A942.
1st successful casting of 6Li PSD at ~1-liter scale.
Mabe et al. AAP 2018.
2012
2013
2016
2019
2021
2023
2024-present

## Slide 14: Starting small: Feasibility of using SiPM arrays SANDD/iSANDD
thermal neutrons
[data with 252Cf source]
First system to show PSD in segmented fully instrumented detector with SiPM arrays (128 channels)
Nucl.Instrum.Meth.A 942 (2019) 162334
Nucl.Instrum.Meth.A 1006 (2021) 165409
Central module of SANDD
64 bars with SiPM arrays
gamma-rays
fast neutrons

## Slide 15: Adding compact electronics
Neutron imaging shows promise but the PSD in QT extraction readout is inferior to full-waveform readouts.
Nucl.Instrum.Meth.A 1046 (2023) 167624
Nucl.Instrum.Meth.A 1057 (2023) 168699
PET-scanner 256-channel SiPM-readout electronics (expandable beyond 1,000 channels)
Future multi-channel detectors would require low-power, low-cost, fast-timing electronics
PSD determination using split signals — Head and Total
HEAD
TOTAL
Qtail = Qtotal – Qhead

## Slide 16: Advancing towards practical aboveground systems — ROADSTR
Each module has 4 scintillator segments.
Each scintillator segment: EJ-299-50 bar
55mm X 55mm X 50 cm
with dual-ended 2” PMT readout
(H11284-100 assembly, optical grease EJ-550)
PROSPECT-style 6 x 6 array realized in 6Li PSD plastic
60-kg prototype using scaled-up Eljen EJ-299-50
Characterizing scintillator properties & performance
Understanding
backgrounds
Nucl.Instrum.Meth.A 1050 (2023) 168093
Nucl.Instrum.Meth.A 1069 (2024) 169916

## Slide 17: PROSPECT-style IBD-like event selection: position, timing, and PSD
PSD
PROMPT:
E: (1, 7.5) MeV
PSP: outside magenta region
PSD
DELAYED:
E: ±3 sigma energy mean
PSP: ±2 sigma PSP mean
PROMPT-DELAYED position and timing:
XY: same or in adjacent 8 segments
Z: 15 cm in Z
T: (1.2, 100) us

## Slide 18: Projected performance if deployed at 25 m, ~3GWt
Encouraging results for a 60-kg detector!
208Tl: 2.6 MeV
40K: 1.4 MeV
12C* 4.4 MeV

## Slide 19: ROADSTR background studies in different configurations
ROADSTR is able to measure neutron-capture correlations — detailed background study is under preparation.
— lead bricks
— poly stack
— bare
— basement
no shield + O(10) mwe
— lead+bpoly
— lead bricks: naturally increase correlated neutron background (muon-induced spallation)
— lead+bpoly: adding bpoly reduces both neutron multiplicity and correlated component
— bare: inside the main borated-polyethylene (bpoly) shield
— poly stack: neutron capture multiplicity similar to bare, while prompt backgrounds slightly reduced
— basement: significantly lower backgrounds, while neutron component is increased
Multiplicity of thermal-neutron-capture
candidates within a 100-us window
IBD-like correlated backgrounds

## Slide 20: CASC-NN* — Test site transparency Ensuring that there are no neutrinos (no fissions)
ROADSTR is currently taking data at the Nevada Test Site to better understand backgrounds.
CONFLUX software: arXiv:2503.18966
Connection to the original proposal by Reines et al.
* Comprehensive Antineutrino Solutions for Contemporary Nonproliferation Needs

## Slide 21: ROADSTR summary
Important lessons learned to proceed to the larger detector!
60-kg system constructed and operational, taking data since 2022
Technology cooperation with Eljen (scaled-up EJ-299-50 material)
Capable of measuring neutron-capture correlated events
Shows useful sensitivity despite small volume (paved the way to a larger detector)
Only using naturally occurring backgrounds for calibration (cosmogenic muons, neutrons, BiPo, 12B beta)
Currently deployed in P-tunnel (test site transparency)

## Slide 22: Going to ton-scale. Meet: Mobile Antineutrino Demonstrator
Hybrid 2D + 3D approach in a shipping container
2D: 6Li+PSD
8x8 bars (EJ-299-50)
Each 6 x 6 x 100 cm3
128 PMTs
0.2 m3
3D: LiZnS+WLS
16x16x25 half cubes (EJ-260)
832 PMTs
0.6 m3

## Slide 23: MAD-2D scintillator encapsulation
In ROADSTR, minor PPO leaching was observed, leading to crystal formation on the surface and degradation of TIR. As a mitigation, in MAD, we encapsulate the bar.
Lots of work: encapsulating scintillator in 1-mil tape and reflector
adhesive
film
air
reflector
Scintillator
Acrylic light guide
PMT locating collar

## Slide 24: MAD-2D status and plans
MAD is a multi-institutional project. Stay tuned for more exciting updates.
Finish construction this summer
Integrate in the full MAD
Deploy the full system by the nuclear reactor
Above-ground near-field measurement campaigns
World’s largest 6Li PSD plastic scintillator stockpile

## Slide 25: Modern Neutrino Detectors and recent advances by our LLNL group
And others outside of this talk. Visit NEUTRINOS.LLNL.GOV  to learn more.
Detection medium:
  Plastic PSD Scintillator (Performance of large-scale 6Li-doped pulse-shape discriminating plastic scintillators NIMA 1069 (2024) 169916)
  Liquid PSD (6Li-loaded liquid scintillators produced by direct dissolution of compounds in diisopropylnaphthalene NIMA 1054 (2023) 168389)
  Water (A long path-length optical property measurement device for highly transparent detector media JINST 18 (2023) 09, P09004, Exclusion and Verification of Remote Nuclear Reactors with a 1-kiloton Gd-Doped Water Detector Phys.Rev.Applied 19 (2023) 3, 034060)
  WbLS (Pulse-shape discrimination in water-based scintillators NIMA 1036 (2022) )
Photosensor:
  PMT (Improvement in light collection of a photomultiplier tube using a wavelength-shifting plate NIMA 1040 (2022) 167207)
  MA MCP-PMT (Studies of MCP-PMTs in the miniTimeCube neutrino detector, AIP Adv. 8 (2018) 9, 095003)
  MA MCP-PMT (LAPPD) (next in this talk)
  SiPM (A prototype for SANDD: A highly-segmented pulse-shape-sensitive plastic scintillator detector incorporating silicon photomultiplier arrays NIMA 942 (2019))
Electronics:
  Feature-extraction (Q/T) (Calibration of a compact ASIC-based data acquisition system for neutron/γ discrimination and spectroscopy with organic scintillators NIMA 1057 (2023) 168699)
  Full-waveform (next in this talk)
Data analysis / simulations / ML:
  GEANT4 / RAT-PAC (Scalability of Gadolinium-Doped-Water Cherenkov Detectors for Nuclear Nonproliferation Phys. Rev. Applied 18, 034059 , Physics-informed machine learning approaches to reactor antineutrino detection, Directional response of several geometries for reactor-neutrino detectors Phys.Rev.Applied 22 (2024) 5, 054030, Ratpac-Two v1.0.0 https://doi.org/10.11578/dc.20240620.8 )
LLNL triple-PSD in water

## Slide 26: Water-based detection
20 km
60 km
This part of the talk will focus on the water-Cherenkov detection and instrumentation.
Key to scaling to O(1 kt) detectors
Factor of a 1,000 less photons compared to scintillators
Can we used Gd-doped water for far-range reactor monitoring?
New instrumentation (WbLS/LAPPD/electronics)
AIT-WATCHMAN LLNL group (circa 2019)
1-ton prototype
Map to show scale.

## Slide 27: A 50-MW reactor in different geographical locations
Three locations selected — range largely dominates by the world’s background.
Phys. Rev. Applied 18 (2022) 034059.

## Slide 28: Sensitivity to detect a 50-MW reactor
Detecting a small 50-MWt reactor at a large distance depends primarily on the world reactor background at that location.
Phys. Rev. Applied 18 (2022) 034059.

## Slide 29: Instrumentation with LAPPDs LAPPD gen 1 and gen 2 — main difference
The new design allows for custom size and shape of anodes (pixelization) but how to read them?
Strips  Pads
Cross  Ribs
Intern James Foot holding LAPPD gen 2 #133
64 SMA connectors at the back and 5 SHV connectors.

## Slide 30: Fast-timing: miniTimeCube era and why we need fast timing
For pure liquid scintillator we likely don’t worry (scintillation dominant), but for WbLS it is valuable.
Fast-timing allows better track reconstruction
Cherenkov and Scintillation light separation
Trade-offs: pixel size, photocoverage, and cost
Cherenkov light in mTC (MA MCP-PMTs)

## Slide 31: Electronics
Connection to UH: Prof. Gary Varner’s dream of “oscilloscope on a chip”.
Can we reach the $10/channel?
How many channels?
Readout in situ?
4-channel AARDVARC eval board (SN 000!)
8-channel IceRingSampler
Track&Hold principle

## Slide 32: Test stand for LAPPD gen 2 at LLNL
The setup is robust and allows for X-Y alignment of the laser beam.
Picosecond laser
Collimators
1:1 splitter
XY stepper motor
Automated scans
LED and laser
Laser fiber
from idea to implementation:
laser

## Slide 33: SPE data with fast Tektronix scope and picosecond laser
Gain: 106 – 107. Jitter: sub-100 ps (single pad), ~100 ps (multipad).
Time delay with respect to laser controller
Time delay between two pixels
Scope traces

## Slide 34: SPE data with NaluScope (AARDVARC 000 SOC)
This is the first time LAPPD gen 2 has been readout with AARDVARC SoC.
Nalu electronics tour
Time delay between two pixels
Waveforms (AARDVARC)

## Slide 35: Current work on LAPPD and fast-timing readout
Photosensors and fast-timing electronics are advancing.
First Readout of LAPPD Gen 2: Successful integration with AARDVARC and HDSoC.
Initial Test Results: Promising performance of new photosensors and electronics.
Future Development: Significant R&D efforts anticipated for a full-scale detector.
Ongoing Tests at LLNL: Cross-talk evaluation.
Looking ahead:
Exploration of New Ideas: Focus on cost-effective underwater and ground detectors.
Development of Test Stands: For photosensors, electronics, and detection media.
R&D Initiatives: Investigating novel techniques, materials, and engineering solutions.
Utilization of Simulation and High-Performance Computing: To enhance detector design and performance.

## Slide 36: Applied Antineutrino Physics workshops
Repository of 20+ years of material.
https://www.phys.hawaii.edu/aap/
https://arxiv.org/abs/2411.13461
# | Year | Venue | Website | Materials
1 | 2004 | Hawai’i | https://www.phys.hawaii.edu/~jgl/nacw.html | Presentations
2 | 2005 | Hawai’i | https://inspirehep.net/literature/1644476 | 
3 | 2006 | Livermore | https://neutrinos.llnl.gov/workshops/aap2006 | Presentations
4 | 2007 | Paris | https://inis.iaea.org/collection/NCLCollectionStore/_Public/39/107/39107638.pdf | AAP2007
5 | 2009 | Angra | https://www.cbpf.br/~angra/files/AAP2009/ | Presentations
6 | 2010 | Sendai | https://www.awa.tohoku.ac.jp/AAP2010/ | Presentations
7 | 2011 | Vienna | https://apc.u-paris.fr/APC_CS/Conferences/AAP2011/Program.html | Presentations
8 | 2012 | Hawai’i | https://www.phys.hawaii.edu/~jgl/AAP/AAP_2012_Agenda.htm | Presentations
9 | 2013 | Seoul | https://indico.cern.ch/event/245969/ | Presentations
10 | 2014 | Paris | http://aap2014.in2p3.fr/ | Presentations
11 | 2015 | Virginia | http://aap2015.phys.vt.edu/ Timetable at Virginia Tech Indico | Presentations
12 | 2016 | Liverpool | https://hep.ph.liv.ac.uk/aap2016/ | Presentations
13 | 2017 | Mumbai |  | 
14 | 2018 | Livermore | https://neutrinos.llnl.gov/workshops/aap2018 https://arxiv.org/abs/1911.06834 | Presentations
15 | 2019 | Guangzhou | https://spe.sysu.edu.cn/aap2019/ Timetable at CERN Indico | Presentations
16 | 2023 | York | https://indico.ph.liv.ac.uk/event/1195/ | Presentations
17 | 2024 | Aachen | https://aap2024.physik.rwth-aachen.de/ | 

## Slide 37: IBD directionality — MTV consortium
Stay tuned (more interesting work is coming up)
Phys. Rev. Applied 22 (2024) 054030

## Slide 38: Conclusion
Mahalo nui loa, John!
The field of Applied Antineutrino Physics is advancing.
Strong connection to Hawai`i
6Li PSD plastic scintillators and fast compact high-channel-density electronics offer unique capabilities for reactor antineutrino monitoring.

## Slide 39: Back-up

## Slide 40: CANS-NN Test Site Transparency
Multiple technologies are currently being evaluated for test site transparency and maritime reactors.