## Slide 1: How IceCube got its Digital Mojo working Or, the story of the Little Chip that Could
David Nygren
University of Texas at Arlington

## Slide 2: How IceCube got its Digital Mojo working Or, the story of the Little Chip that Could
David Nygren
University of Texas at Arlington

## Slide 3: Once upon a time...
... I was visited by a Greek friend of mine, Leonidas Resvanis, who invited me to help him realize his dream of neutrino astronomy in the Mediterranean...

## Slide 4: The challenges he faced were very tall
To demonstrate NESTOR, Leo was planning the deployment of one “floor” at the excellent site near Pylos, Greece.
Twelve PMT waveforms must be captured with high sampling frequency and dynamic range and very low power.

## Slide 5: The challenges were very tall.
ADCs at the time (1990’s) for this purpose were very power hungry...
Instead, maybe a UCB student project I had by chance seen at LBL might be of interest...
This was an ASIC designed by Stuart Kleinfelder for his MS degree.

## Slide 6
(1996): A switched capacitor array we called the
Analog Transient Wave Recorder! (ATWR)
Designer: Stuart Kleinfelder, LBL, now Professor in EE, UC Irvine

## Slide 7
(1996): A switched capacitor array we called the
Analog Transient Wave Recorder! (ATWR)
Stuart’s Master’s thesis, UCB
***
Switched-capacitors: low power
Three input channels
256 samples per channel
synchronous sampling: variable from 200 - 1000 MHz
2.5 µm double-poly technology!
10 bit S/N, but:
No internal ADC: Slow readout!

## Slide 8: We used this ASIC for NESTOR
Joshua Sopher of LBL did the overall design for deployment at the NESTOR site near Pylos.
I had somehow gotten money from NSF ($150K ?) for this... (Or maybe it was for something else...)
It all worked; data sent back to shore allowed full reconstruction of downward going muons.

## Slide 9: AMANDA  IceCube
It was around this time that I had become somewhat involved with AMANDA and the IceCube transition
AMANDA very successful... but:
  PMT pulses after 2 km cable - not so good
  Optical fiber: PMT pulses much better, but...
    Dynamic range still not so good
    Optical cables: not so robust (or cheap) either...
    Optical calibration: not so stable...
    Not so pleasant to deploy two down-hole cables

## Slide 10: “What does IceCube really need?”
High dynamic range:
  deposited energy may vary by ~106
Lowest possible power dissipation
  Incompatible with waveform capture?
Complex waveform information:
  Ice: absorption small, scattering large
Let’s find out – use the ATWR
  two pre-prototype Digital Optical Modules!

## Slide 11
What’s this?

## Slide 12
What’s this?
This is one of
two primitive
DOMs made
at JPL!

## Slide 13
What’s this?
This is one of
two primitive
DOMs made
at JPL!
Why JPL?

## Slide 14
What’s this?
This is one of
two primitive
DOMs made
at JPL!
Why JPL?
“Because that’s where the money is!”*
* Willie Sutton

## Slide 15: Seed Money
In addition to JPL’s support (~$100K) Buford Price and Francis Halzen also contributed to the construction of these two proto-DOMs at JPL.
And they worked!

## Slide 16: AMANDA J-B-W DOM
7.5us
132ns
Thanks to
Tim Miller and Doug Lowder

## Slide 17: Suddenly, there was KamLAND!
Stuart Freedman (LBL/UCB) came to me and asked how “we” might usefully get involved with KamLAND.
“Why not use Stuart’s ASIC to do the electronics and DAQ for KamLAND?” This became a $6M project...
I came to Hawaii and made a pitch for that showing that we used the ATWR successfully for NESTOR.
We were accepted for this task, but I have the impression that our KamLAND friends were wary.
Stuart implemented an internal Wilkinson ADC and the ATWR became the ATWD. Much better!

## Slide 18: ATW “R”  ATW “D”
A 128-channel common-ramp Wilkinson ADC was added by Stuart K.
This sped up the readout greatly.

## Slide 19: All that worked too.
The electronics for KamLAND was completed by Thorsten Stezelberger and another LBL engineer.
Delivery was hampered by bad production quality, but the system was used by KamLAND for many years.
On the basis of success in KamLAND, we could propose to use the ATWD as the enabling element...

## Slide 20: ...For IceCube
Analog to Digital conversion of IceCube
Each optical module must become a complete semi-autonomous data acquisition platform, linked in an all-digital network with asynchronous DAQ.
A complete departure from the AMANDA framework.
A complete systemic transformation!

## Slide 21: Scary things
“Let’s make 5000 complex tethered satellites and bury them forever in ice”
“Will the cold keep them from working?”
“Nothing like this has ever been done”
“What if we make a mistake we can’t fix?”

## Slide 22: Waveforms are useful!
Get to work on realizing a digital string
  but how?
NSF: $325K for AMANDA string 18
  grant to George Smoot, UCB
Start: meeting at LBL, November 1998
  tremendous motivation to do this
Karle: “Let’s make string 18 a hybrid”
  what’s one more back-breaking feature?

## Slide 23: “Main board” for AMANDA String 18 40 Optical Modules, January 15, 2000
String 18: Jerry Przybylski
Jozsef Ludvig

## Slide 24: Digital Optical Module Block Diagram
FPGA
CPU
CPLD
Flash
Flash
PMT Power
SDRAM
SDRAM
ATWD
ATWD
fADC
DAC
Monitor
& Control
LPF
LC
x16
x2
x0.25
Flasher
Board
Pulser
DACs & ADCs
Corning Frequency Ctl (was Toyocom)
4Mb 4Mb
16Mb
16Mb
+/-5V, 3.3V, 2.5V, 1.8V
64 Bytes
Delay
Trigger (2)
ADC
Oscillator
20 MHz
40 MHz
MUX
(n+1)
(n–1)
DOR
OB-LED
x 2.6
x 9
10b
10b
10b
10b
8b
32b
16b
8b
8b, 10b, 12b
DP Ram
1 megabaud
DC-DC
Configuration
Device
8Mbit
GTP, LBNL, 26 Mar, 2004

## Slide 25: Digital Optical Module Block Diagram
FPGA
CPU
CPLD
Flash
Flash
PMT Power
SDRAM
SDRAM
ATWD
ATWD
fADC
DAC
Monitor
& Control
LPF
LC
x16
x2
x0.25
Flasher
Board
Pulser
DACs & ADCs
Corning Frequency Ctl (was Toyocom)
4Mb 4Mb
16Mb
16Mb
+/-5V, 3.3V, 2.5V, 1.8V
64 Bytes
Delay
Trigger (2)
ADC
Oscillator
20 MHz
40 MHz
MUX
(n+1)
(n–1)
DOR
OB-LED
x 2.6
x 9
10b
10b
10b
10b
8b
32b
16b
8b
8b, 10b, 12b
DP Ram
1 megabaud
DC-DC
Configuration
Device
8Mbit
GTP, LBNL, 26 Mar, 2004

## Slide 26
Jerry P set up a test bench for oscillators so we could measure the stability of various products
The winner:
Toyocom
incredible performance!

## Slide 27: Rev 4.2

## Slide 28
Reciprocal
Active
Pulsing
Calibration
“RAPCal”
- Bob Stokstad
A few times a second, each DOM receives and sends a special pulse to measure the cable length and phase of the local quartz oscillator

## Slide 29
Bob Stokstad - with string 18 module

## Slide 31
Thorsten Stezelberger,
on his way to make some on-site hardware calibrations

## Slide 32: Kalle Sulanke (McMurdo?)

## Slide 33
Don Hartill
Albrecht Karle
Kael Hanson

## Slide 34: We Won!
We, somehow, survived countless reviews.
IceCube DAQ systems continue to work well
Stop that $#& ¥≠ power-cycling!

## Slide 35: We Won!
We, somehow, survived countless reviews.
IceCube DAQ systems continue to work well
The Little Chip that Could, and Did is a great story, made possible by many people.
Stop that $#& ¥≠ power-cycling!

## Slide 36: We Won!
We, somehow, survived countless reviews.
IceCube DAQ systems continue to work well
The Little Chip that Could, and Did is a great story, made possible by many people.
NESTOR  KamLAND  IceCube was not a planned sequence, but it all worked out !
Stop that $#& ¥≠ power-cycling!

## Slide 37
Thank you
We recall that this experimental field was started by
John Learned, with DUMAND