## Slide 1: BINP tau charm plans and other projects in Turkey/China
A. Bogomyagkov
BINP SB RAS, Novosibirsk

## Slide 2: History
1993, Dubna JINR (Ecm= 2 GeV, L=9.41032 cm-2 sec-1)
1994, Argonne National Laboratory (Ecm=3-5 GeV, L= 1033 cm-2 sec-1 )
1995, BINP, round beams (Ecm= 2.0-4.2 GeV, L= 1033 cm-2 sec-1)
1996, Spain & France (Ecm= 4 GeV, L= 1033 cm-2 sec-1)
1997, Beijing IHEP (Ecm= 2.0-4.2 GeV, L= 1033 cm-2 sec-1)

## Slide 3: BEPC II
Two-ring e+e- collider in the tau-charm energy region (Ecm = 2.0-4.2 GeV).
Upgrade of BEPC, operating for HEP since May 2009.
“One machine, two purposes” – source of SR
Design luminosity 1033 cm-2 sec-1 at 1.89 GeV.
Beam current 0.93 A.
Circumference 240.4 m.

## Slide 4: BEPCII layout

## Slide 5: BEPC II performance

## Slide 6: BEPC II future plans
More detailed optics measurement & correction is being done
We still not obtain some luminosity improvement by suppressing the parasitic beam‐beam interaction
We’ll try to achieve higher luminosity by more detailed optimization, higher beam current and lower βy.

## Slide 7: Turkic Accelerator Complex (TAC)
Linac-ring type charm factory
  L= 1.41035 cm-2 sec-1
Detector to search for charm physics:
  CP violation and mixings of D0-mesons
  new physics effects in the rare decays.
Synchrotron light source based on positron ring
Free electron laser based on electron linac

## Slide 8: TAC Super Charm Factory

## Slide 9: TAC charm factory parameters
Parameter | e--linac | e+-ring
Energy, GeV | 1.00 | 3.56
Particles per bunch, 1010 | 2 | 20
 function at IP, mm | 80/5 | 80/5
x/y/z, m/m/mm | 36/0.5/5 | 36/0.5/5
Beam current (A) | 0.48 | 4.8
Circumference, m |  | 600
Crossing angle, mrad | 34 | 
Collision frequency, MHz | 150 | 
Luminosity, cm-2s-1 | 1.41035 | 

## Slide 10: TAC Super Charm Factory plans
The TAC SCF was presented to ECFA 2011 as a cornerstone of the TAC project in terms of its originality and competitiveness. In order to gain more experience on the accelerator and detector and data analysis issues, they do consider to collaborate within the global projects on flavor factories.
In 2011, they have joined BES III collaboration facilitated in Beijing China.
A technical report of SCF@TAC will be completed in 2013.

## Slide 11: Super-c-tau in Novosibirsk
E = 700 – 2500 MeV
Round beams L = 1034 cm-2s-1
Monochromatization L ~ 1032 cm-2s-1
Long. Polarization L ~ 1034 cm-2s-1
Transverse polarization for precise energy calibration

## Slide 12: Super-c-tau: general
Two rings with CRAB waist
  Single interaction point
L = 1035 cm-2s-1 at 2 GeV
  Preserving emittance and damping times through the whole energy range to optimize the luminosity
  Sub-mm y at IP
Electrons are polarized longitudinally
  Polarized electron source
  2.5 GeV full energy linac
  5 Siberian snakes to obtain the longitudinally polarized electrons for the whole energy range
    to study  at threshold
    to study c baryons
Variable energy Ecm= 3  4.5 GeV (from J/ to charm barions)
Energy calibration with medium accuracy (Compton backscattering (5  10)10-5)

## Slide 13: Super-c-tau: scientific case

D
Ds


## Slide 14: Super-c-tau: scientific case
Charmonia
Spectroscopy, BFs
Light hadron spectroscopy
J/ rare decays
…
Charm
Spectroscopy
(Semi)leptonic decays
Rare decays
Mixing
CP violation
…
Tau
Spectral functions, BFs
Lorentz structure
CP violation
LFV decays
…
Charm baryons
BFs
Semileptonic decays
CP violation
…

## Slide 15: Super-c-tau: parameters
Beam Energy | 1.0 GeV | 1.5 GeV | 2.0 GeV | 2.5 GeV
Circumference | 780 m |  |  | 
Emittance hor/ver | 8 nm/0.04 nm @ 0.5% coupling |  |  | 
Damping time hor/ver/long | 30/30/15 ms |  |  | 
Bunch length | 16 mm | 11 mm | 10 mm | 10 mm
Energy spread | 10.1·10-4 | 9.96·10-4 | 8.44·10-4 | 7.38·10-4
Momentum compaction | 1.00·10-3 | 1.06·10-3 | 1.06·10-3 | 1.06·10-3
Synchrotron tune | 0.007 | 0.010 | 0.009 | 0.008
RF frequency | 508 MHz |  |  | 
Harmonic number | 1300 |  |  | 
Particles in bunch | 7·1010 |  |  | 
Number of bunches | 390 (10% gap) |  |  | 
Bunch current | 4.4 mA |  |  | 
Total beam current | 1.7 A |  |  | 
Beam-beam parameter | 0.15 | 0.15 | 0.12 | 0.095
Luminosity | 0.63·1035 | 0.95·1035 | 1.00·1035 | 1.00·1035

## Slide 16: Super-c-tau: optics
IP: y=0.8 mm
x=40 mm

## Slide 17: Super-c-tau: main ring

## Slide 18: Super-c-tau: CRAB waist
q
z
e+
e-
x
IP
Sext
M
m
Sext
CP
βy
(P.Raimondi 2006)

## Slide 19: Super-c-tau: CRAB waist

## Slide 20: Super-c-tau: facility artist view

## Slide 21: Super-c-tau: facility cite

## Slide 22: Super-c-tau: final focus
QD0
Detector Yoke
QF1
Anti Solenoid
e-
e+
Cryostat
Compensation Solenoid

## Slide 23: Super-c-tau: final focus

## Slide 24: Super-c-tau: final focus
SC iron yoke twin aperture magnet
Excitation current 8.5 kA·turns
Single aperture 2 cm
Gradient 10.7 kGs/cm
Length 20 cm
Prototype is being manufactured.

## Slide 25: Super-c-tau: injection facility

## Slide 26: Super-c-tau: construction cite
A.Bogomyagkov (BINP)
26
Ready-built tunnel
FF region
Technical reg. (RF and injection)
Damping wiggler sections

## Slide 27: Super-c-tau: conclusion
The lattice, meeting all main requirements is ready.
FF key element, twin-aperture SC quadrupole prototype is being manufactured.
Prototype of the damping wiggler is ready.
Civil construction is under way.
  injection facility is under commissioning, tunnels for linac and injection lines are ready, bulk of the facility solutions are based on existing wares and technologies.
Detailed machine design and beam dynamics simulation is in progress.
Project is being considered in government committee.