## Slide 1: CAD style figures needed
For NIM paper:
  Dcube-micro sideview (Marc)
    https://www.phys.hawaii.edu/elog/DCube/39
for BEAST TDR:
  BEAST T0 (Marc)
  BEAST T1 (Marc)
  BEAST T2 (Marc)
  Schematic of TPC system w/ services (Sven)
  CAD or G4 model of single TPC (Kamalu?)

## Slide 2: (new version)
 | w/o QCS, w/o solenoid | w/ QCS, w/o soldenoid | w/QCS, w/ solenoid , No SVD, PXD
Beam pipe | 4 cm (ID?) | ? | Mockup
PIN Diodes | Y | Y | Y
Beam abort: PIN? Radfet? Polycrystal, single channel diamonds? | N | N | Y
Micro-TPCs | 2 prototypes | Y | Y, in SVX dock
Synchrotron x-ray measuremnet |  |  | Thick PXD ladder? SDDs?
BGO | Y | Y | Y
CDC prototype | N | Y | N
SVD, PXD ladders & monitors | N | N | Y
FE-I4 pixels w/ diamond sensor near IP | Y | Y | No space
Scintillator squares/ PIN dioes (tbd) 3x8x2? |  |  | Y? tbd
Thermal neutron detector? |  |  | Y? tbd
BEASTII-T0
BEASTII-T1
BEASTII-T2
Jeep way 1,1’,2
Jeep way 1,1’
Jeep way 1,2 (not 1’)
Phase 1
Phase 2

## Slide 3: BEASTII-T0
CAD drawing by Kanazawa-San
/ Marc Rosen
Expect no luminosity during this stage
Mostly high levels of beam-gas BG, possibly some Touschek
Main BEAST goal: Measure radiation levels to determine when it’s safe to roll in Belle

## Slide 4: BEASTII-T1
Expect collisions, production of all beam BGs
Many BG measurements BG possible, allowing validation of simulation
Plenty of space for BEAST subsystems
Interesting stage for BEAST, but in scenario A we would skip this stage

## Slide 5: BEASTII-T2
Closest to final SuperKEKB/Belle 2
Very limited space for BEAST detectors
Good for VXD measurements and related
Place some detectors in available VXD dock space

## Slide 6: Reminder of BEAST TDR schedule (expected deliverables in red)
April 19th:
  Draft specifications for each beast subsystem
    We need this soon so that Marc Rosen can make a BEAST cad drawing
  BEAST TDR chapter outlines
    E.g. list of sections and expected figures
   Review/dicuss during April 23rd BEAST meting
May 1st: BEAST TDR draft
  Including preliminary or final figures
  Review and discuss outstanding issues during May 7th BEAST meeting
May 24th: BEAST TDR final version: HARD DEADLINE
  Sven to integrate w/ US Belle II TDR, send out for final proofreading
May 31: Completed US BelleII TDR

## Slide 7: Micro TPC system Draft Specifications List of TDR Figures
Sven Vahsen, Igal Jaegle

## Slide 8: Draft Specifications of Micro-TPC System red: to be determined/checked
who will provide it, install it, operate it: U. Hawaii group; Vahsen, Jaegle (postdoc), Hedges (grad student), Seong (grad student), Rosen (engineer), X (postdoc)
expected physics measurements: fast-neutron flux, angular distribution if achievable during T2
  goals
    discriminate different beam backgrounds so that we can predict neutron flux at higher luminosity
    verify / tune normalization and angular distribution of neutron flux in simulation
space requirements and location in T0,T1,T2
  Approx. dimensions of each TPC: 6"x4"x30cm
  2 TPCs during T0 (1 forward, 1 backward)
  8 TPCs during T1, T2
  Locations of center of TPCs:
    backward: r=32 cm, z=-122cm
    Forward: r=37cm, z=199 cm
    Four phi positions: 0,90,180,270 degrees
30 cm
6“
4“

## Slide 9: Draft Specifications of Micro-TPC System red: to be determined/checked
DAQ: Input/output signals per TPC
  Digital I/O of 4FE-I4 chips (trigger,LVDS in/out, combined ground)  21 per channels per TPC
  Analog signal from copper anode: 1 coax per TPC
Services
  LV: ~2V, analog, digital  4 wires if common power (parallel or serial), 16 wires if individual)
  HV: 5kv: 4 CH + GND, 30 kv (field cage): 3 CH + GND
  Gas in/out
  Cooling: not required
  whether you can take care of them all, or need KEK to provide: will/may ask KEK to provide gas
Service connections
  32-pin or 50-pin mil spec LV connection on KF40 feedthough
  8 HV on KF40 feedthrough (up to 2 SHV)
  3 swage lock (gas in/out, overpressure)
  1 KF 40 pump port for quick purge
Cable thicknesses, pipe diameters
  Gas: ¼” stainless steel tubing
  Cables: tbd
max distance from sensors to closest part of DAQ system / electronics, so that we can reserve space. Location of DAQ.
  ~20m (need to check if OK for LVDS and analog readout)
6”
4”
2.08”
HV (<=8 pins)
LV+DAQ
(<=50 pins)
KF40
to vacuum pump
Pressure relief
gas in
gas out

## Slide 10: List of Figures for micro-TPC chapter
Schematic of TPC system w/ DAQ and services (Sven)
CAD or G4 model of single TPC (Marc, Kamalu)
TPC Acceptance criteria vs pre-prototype measured performance
  Angular resolution (Ilsoo)
  Gain resolution (Tom)
  Energy resolution (Ilsoo)
  Simulated neutron efficiency (Igal)
  Demonstration of neutron detection (Ilsoo & Sven)
Simulated neutron & particle flux
  In Belle frame (Igal, Ilsoo, Michael)
    Rate of neutrons through TPC versus momentum, theta, phi
  In TPC frames (Igal)
    Expected theta, phi distributions, time-normalized, for each beam BG
    Split up into: He-recoil in gas, alphas, protons, EM, other BG
TPC efficiency vs momentum (for which direction?) (Ilsoo, Igal, Sven)
  Neutrons
  Electrons
  muons

## Slide 11: Schematic of TPC system
(figure below shows current lab prototyping system, still need to update for BEAST system)